C90 Fuel Sending Unit Repair

My sending unit was intermittent showing empty on the gauge even after filling. This is the repair to the sender to help prevent you from having to purchase a new fuel pump at a retail cost of $560.00. First you are going to need a 2/56" thread die and some nylon nuts & washers to match. I got the nuts and washers from my local hobby shop. They were out of stock on the die so I had to get it at a local tool shop. Cost me less than $10 for the die, nuts & washers. I had a die holder already so I didn’t need to purchase one. If you can’t find the die & nuts locally you can try online @ Tower Hobbies. The part numbers are as follows.

Die: LXR765

Die Holder: LXR768

Nylon Nuts: LXK026

Washers: LXK035

I broke down the pump and removed the float from the sending unit.

Then I put the float in my vise and started threading the end. I kept going forwards & backwards till I threaded about 5/16".

I then reassembled the float to the sending unit. I will say be very careful with the wires to the sending unit as they a very thin, 22 gauge I think, and will break quite easily. They are covered with heat shrink on both ends so you will most likely not know it unless you pull on them kind of hard. I didn’t use a spring washer behind the nut as all I could find at my local Ace were just a little too big in overall size. I just kept snugging up the nut till there was very little play and it was in no way coming close to not letting the float move freely.

Then I reassembled the entire pump and reinstalled it.

The fuel gauge now works properly again. This was a very easy repair and you could do it in less than 2 hours if you have the parts needed. I hope this helps anyone having an intermittent problem with their sending units.

Chris